## Slide 1: Mexican Society for Geotechnical Engineering
Sociedad Mexicana de Ingeniería Geotécnica, A. C.

## Slide 2
Mexico:
“Paradise of Soil Mechanics”
Karl Terzaghi

## Slide 3
Mexico City clay
Notes: Open pit 4.6 m deep. Pozo a cielo abierto de 4.6m de profundidad

## Slide 4
Property | Value
Void ratio (e) | 5−10
Porosity (n) | 0.83−0.90
Water content (w) | 220−420%
Liquid limit (wL) | 110−458%
Plastic limit (wP) | 37−116%
Plastic index (IP) | 73−342%
Permeability (k) | 1×10-7cm/s
Compressibility index Cc | 3−8
Undrained modulus E | 4000−7000 kPa
Undrained shear strength cu | 15−35 kPa
Sensitivity | 8
Internal friction angle | 34−41 degrees
Shear wave velocity | < 100 m/s
Typical properties of Mexico City clay
Mexico City lacustrine clays unusual properties have been a matter of curiosity
and a subject of research for many outstanding geotechnical engineers

## Slide 5
A. Casagrande referred to the famous book by R.J. Marsal and M. Mazari as “the bible”

## Slide 6
Mexico City lacustrine zone presents a regional subsidence
that has reached 13.5m in some areas (1862-2013)
Subsidence of Mexico City

## Slide 7
Dr. Nabor Carrillo provided a scientific explanation of Mexico
City subsidence in 1948
Regional subsidence
Carrillo, N. 1948. “Influence of Artesian Wells on the Sinking of Mexico City”, Proc. Second International
Conference on Soil Mechanics and Foundation Engineering, Rotterdam, Nederland.
Dr. Nabor Carrillo

## Slide 8: Behavior of foundations in Lake zone
Special foundations systems are used in Mexico City to avoid excessive settlement of surface foundations or apparent protruding of point bearing foundations
Upper clay formation
Lower clay formation

## Slide 9
1911
Dh
2010
Apparent protruding of
point-bearing piled foundations

## Slide 10
“Compensated Friction-Pile Foundation to Reduce the Settlement of the Highly Compressible Volcanic Clay of Mexico City”, Proceedings Fourth International Conference on Soil Mechanics and Foundation Engineering, Vol. II, pp. 81-86, London, England, August.
Leonardo Zeevaert introduced innovative design methods for compensated foundation, piled raft foundations and compensated-friction pile foundations
Dr. Leonardo Zeevaert Wiechers

## Slide 11
Manuel González Flores introduced “Control piles” equipped with a mechanical system for controlling loading on individual piles and foundation differential settlements
González Flores, M., 1948, “Level control in buildings by means of adjustable piling”,
Proceedings, Second International Conference on Soil Mechanics and Foundation Engineering,
Rotterdam, Vol. IV, p. 152
Control piles
Manuel González Flores

## Slide 12
During the 1990-2000 period, the large differential settlements of the Metropolitan Cathedral of Mexico City were corrected by a team of Mexican Engineers by the sub-excavation technique, a procedure that was subsequently adopted also for the Pisa Tower…
Geotechnical team:
Enrique Tamez
Enrique Santoyo
Efraín Ovando
Metropolitan Cathedral

## Slide 13
-200
-100
0
100
200
CU EW COMP.
.
ACC [cm/s2]
-200
-100
0
100
200
0
20
40
60
80
100
120
140
160
180
200
SC EW COMP.
TIME (s)
Site effects in seismic conditions in Mexico City
September 19th, 1985 macroearthquake
Rock
Soft clays
Extraordinary site effects were observed in Mexico City during the 1985 earthquake

## Slide 14
Some foundations suffered severe damage
during the 1985 earthquake
Auvinet, G., Pecker, A. & Salencon, J., 1996, “Seismic bearing capacity of shallow foundations in Mexico City during the 1985 Michoacan Earthquake”, Proceedings, Eleventh World Conference on Earthquake Engineering, (CDROM), Acapulco, Mexico, July.
Romo, M.P. and Auvinet, G., 1992, “Seismic behavior of foundations on cohesive soft soils”, in “Recent Advances in Earthquake Engineering and Structural Dynamics”, edited by V. Davidovici, Ouest Editions, pp. 311-328, Paris, France.

## Slide 15
Resonant column
A thorough experimental and theoretical research program
was developed following 1985 earthquake

## Slide 16
Computed response spectra, Mexico City
Romo, M.P. and Seed, H. B. (1986). “Analytical modelling of dynamic soil response in the Mexico earthquake of September 19, 1985”, Proc. ASCE Specialty Conf. on the Mexico Earthquakes-1985, Factors Involved and Lessons Learned. Mexico, September.

## Slide 17
“El Infiernillo” Dam
Earth and Rockfill dams in Mexico

## Slide 18
“El Infiernillo” Dam was the first structure of this type to be thoroughly instrumented

## Slide 19
Marsal, R.J. and Ramírez de Arellano, L., 1967, “Performance of El Infiernillo Dam,
1963-1966”, Journal of the Soil Mechanics and Foundations Division, ASCE, July.
Raúl J. Marsal is considered as one of the most important scientists and engineers
behind modern design of earth and rockfill dams
Prof. Raúl J. Marsal

## Slide 20
The largest triaxial cell in the world (T113-25) was built by Marsal in Mexico for Rockfill testing
Marsal, R.J., 1963, “Triaxial apparatus for testing rockfill samples”, Proceedings,
IInd Pan-American Conference on Soil Mechanics and Foundation Engineering, Brazil.

## Slide 21
Triaxial cell T113-25 was the star of the 1969 ICSMFE
(fourth from left: G. Auvinet, Institute of Engineering UNAM)

## Slide 22
The 300-hectare, 6m deep, cooling pond
of the Río Escondido Power Plant in Northern Mexico has behaved satisfactorily without any detectable leakage for more than thirty years thanks to a specially designed clay liner
Artificial Impoundment
Auvinet, G. & Espinosa, 1979, "Impermeabilization of a 300-hectare cooling pond", ASTM Special Technical Publication N0 746, “Permeability and Groundwater Contaminant Transport” pp. 151-167, USA.

## Slide 23
Total length = 62 km
Diameter = 7 m
24 tunnel shafts (from 20 to 155 m deep)
Geotechnical team:
M. Aguilar
G. Auvinet
D. Reséndiz
J.L. Rangel
J.F. Rodríguez
“Emisor Oriente” tunnel, one of the largest tunnel in the world, is now under construction in Mexico valley in challenging geotechnical conditions
“Emisor Oriente” tunnel

## Slide 24
a) Traditional cross section (CFE, 2009)
b) Estimated cross section of water content (virtual)
c) Standard deviation of estimation
Auvinet, G. & Juárez, M., 2012, “Geotechnical Characterization of subsoil along Emisor Oriente Tunnel in Mexico City”, Proceedings, International Conference on Soil Characterization, ICS’4, Porto de Galinhas, Pernambuco, Brazil, Vol. 1 pp. 1273-1281, ISBN 978-0-415-66069-3.
Geostatistical model

## Slide 25: “ISSMGE has not yet had a President from Mexico, from which a great deal of the classical work in our subject developed”
Harry Poulos
(26/11/2012)

## Slide 26
The Mexican Society for Geotechnical Engineering together with ISSMGE Member Societies from:
Argentina
Canada
Chile
China
Colombia
Dominican Republic
El Salvador
Venezuela
support the candidacy of Professor Gabriel Auvinet to the position of ISSMGE President for the 2013-2017 period.
Encouragement messages have been received from many members societies and distinguished personalities from Africa, Asia, Australasia, Europe, North America and South America.

## Slide 27
Professor Gabriel AUVINET
President of ISSMGE Candidate
Geocomputing Laboratory, Institute of Engineering
Torre de Ingeniería, 2nd floor, Circuito Escolar,
Ciudad Universitaria, Mexico, D.F.
e-mail: gauvinetg@iingen.unam.mx
Office phone: +52(55)56233600, ext 8324, Mobile: +52(55)54122915